## Slide 1: Simulating the Value of Vehicle-Grid Integration using a Behaviorally-Realistic Model
Michael Wolinetz
Adjunct Professor, Simon Fraser University
Partner, Navius Research
January 8th, 2017
SFU START

## Slide 2: Limitations of past analyses
Little representation of behaviour or policy impact
Plug-in electric vehicle (PEV) adoption is assumed
VGI participation is assumed (e.g. participation in or utility controlled charging, UCC)
Electricity grid is based on the current grid or an assumed future grid

## Slide 3
Survey Sample:
N=496 in BC
N=289 in AB

## Slide 4: Dimensions of our analysis
Framing: impact of UCC with regard to deep GHG reductions out to 2050
With UCC vs. without UCC of PEVs
Policy scenario (i.e. Simulate impact of strong GHG policy) vs. “forced” scenario (i.e. No consumer behaviour, deterministic policy outcomes: only RE, no CCS)
Case study regions: British Columbia (BC, with large hydro) and Alberta (AB, no large hydro)

## Slide 5: Consumer behavior defines the magnitude of UCC participation
Chart: % light-duty vehicles participating in UCC
| 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
BC, policy scenario | 0.0054022 | 0.026396 | 0.058488 | 0.10837 | 0.16496 | 0.22123 | 0.2595
BC, forced scenario | 0.0080913 | 0.044997 | 0.11317 | 0.23865 | 0.46148 | 0.70686 | 0.89211
AB, policy scenario | 0.0034628 | 0.019165 | 0.048553 | 0.099305 | 0.15285 | 0.20545 | 0.24122
AB, forced scenario | 0.0070022 | 0.043069 | 0.11248 | 0.2424 | 0.46493 | 0.71111 | 0.89553
Not everyone will buy a PEV, not all PEVs will participate in UCC.

## Slide 6: Benefit of VGI: Modest reduction to the price of electricity in a GHG constrained world
Chart: UCC impact on electricity price in 2050, real 2010 $/MWh
| BC, policy scenario | BC, forced scenario | AB, policy scenario | AB, forced scenario
2050 | -0.57436 | -1.6664 | -0.67233 | -7.1401
Forced scenarios:
Everyone buys PEVs
Full UCC participation
No Carbon Capture and Storage

## Slide 7: Potential UCC benefits we did not find:
Value of UCC accruing to PEV owners
Increased PEV adoption
Increased adoption of intermittent renewable generation
Reduced GHG emissions

## Slide 8: Insights
Strong policy is still needed for adoption of PEV and low-GHG electricity generation
Our hunch: Hype followed by disappointment is a risk to development of VGI
VGI should be viewed as one tool among many to provide societal benefit through a smart-grid

## Slide 9: More Information
www.sustainabletransport.ca
www.naviusresearch.com
Wolinetz, M., Axsen, J. & Peters, J. (Under Review). Simulating The Value Of Vehicle-Grid Integration Using A Behaviourally-Realistic Model. Submitted to Environmental Science & Technology.